## Slide 1
BATCH 0A · FOUNDATION
North American Power Markets
Nodal pricing, resource adequacy and a fragmented carbon overlay
Fifteen slides covering the FERC / NERC / state regulatory stack, nodal LMP and its decomposition, congestion rights, capacity markets versus energy-only design, ERCOT scarcity pricing, the data-centre load shock, and the four separate carbon regimes.
Written for a risk practitioner who already knows the European market. Positions verified to 30 July 2026 — four moved materially in the last twelve months.
8 hrs
Foundation study budget within the 80-hour Americas programme
Self-study programme · 6 weeks · 80 hours · 17 market packs · Prepared 30 July 2026
Notes: Batch 0A of a seven-batch build. This deck and its gas twin (0B) are the only two that are not market-specific. The framing throughout is comparative: the reader has completed the EU programme, so every section says what transfers and what does not. The single most dangerous carry-over is the calorific basis - Europe works LHV, North America works HHV - which is covered on slide 13 and is the reason the parameter workbook refuses to return an unlocked unit convention.

## Slide 2
01
How the Americas programme fits together
Two foundation decks, then seventeen market packs on a common template, then environmental markets, consolidation and the quant layer
Chart: Hour budget - 80.5 hours total
| Foundation (0A+0B) | 7 US ISOs @ 3 hrs | 5 gas hubs @ 2.5 | Canada + LatAm | Environmental + consol. | Quant layer
Hours | 8 | 21 | 12.5 | 15 | 9 | 15
1
Batch 1
PJM, ERCOT, MISO - the three archetypes, not the three biggest
2
Batch 2
CAISO, NYISO, ISO-NE, SPP
3
Batch 3
Henry Hub, Permian-Waha, AECO, Northeast, West
4
Batch 4-5
Alberta, Ontario · Mexico, Brazil, Chile+Colombia
5
Batch 6-7
Environmental markets, consolidation, quant layer
Batch 1 is PJM, ERCOT and MISO because they are the three archetypes - a nodal market with a capacity construct, an energy-only market of scale, and a market defined by its seams. The other four ISOs are variations, which is why they compress into Batch 2 at the same hours.
Source: Americas Energy Programme plan, 30-Jul-2026. Europe ran 60 hours over 12 packs; the Americas needs 80 over 17 because gas and environmental markets do not compress into the country packs.
Notes: The hour split is the first place this programme diverges from Europe. In the EU, gas sat comfortably on tab 3b of a country pack because an entry-exit system with virtual hubs is a national object. In North America gas is point-to-point pipeline capacity and the tradable object is the basis between two physical points, which belongs to no single power market - hence five separate gas packs. Environmental markets get the same treatment. Europe has one carbon instrument. The Americas have RGGI, the California-Quebec link, Washington's CCA, no federal price, a REC/SREC compliance patchwork and IRA credits acting as a negative carbon price. That does not fit on a slide.

## Slide 3
02
Who regulates what
Federal versus state - and derivatives sit with a different agency entirely from the one that regulates the physical market
FERC — Federal Energy Regulatory Commission
Approves ISO/RTO tariffs and market rules · interstate transmission and pipeline rates · pipeline certificates · anti-manipulation under Order 670
NERC — reliability
Mandatory, enforceable reliability standards across the US, Canada and part of Mexico, through six regional entities
State PUCs / PSCs
Retail rates · integrated resource planning · siting · RPS compliance · retail choice. Where most decisions that shape a state's generation mix are actually taken
CFTC — derivatives
Futures, swaps and options on power and gas. Dodd-Frank registration, clearing and reporting. A different agency from the physical-market regulator
The jurisdictional fact that shapes the US map
ERCOT is intrastate. It does not cross a state line, so it sits outside FERC's wholesale jurisdiction and answers to the PUCT instead. That is where its design freedom comes from - and it is why the only energy-only market of scale in the world is in Texas.
Where the European analogy breaks
REMIT, EMIR and MiFID II put physical and financial energy markets under one framework. Here they are split between FERC and the CFTC, with a contested boundary. Treating that as a modelling detail is a compliance error, not a modelling error.
Roughly a third of US load sits outside any organised market at all - most of the Southeast and much of the West are vertically integrated utilities with bilateral trade and no LMP.
Sources: FERC Order 670 and EPAct 2005 s.315; NERC standards; PUCT Substantive Rule 25.505. Accessed 30-Jul-2026.
Notes: The layered structure tells you where to look when something changes. Statutory change enters at the top and takes years. FERC order and state PUC rulemaking is the middle layer, takes months, and is where most tradeable rule changes originate. ISO business practice manuals are operational and can move in weeks. The FERC/CFTC split is worth dwelling on. A European risk manager is used to one perimeter covering both legs. Here a physical bilateral is FERC-jurisdictional and its financial hedge is CFTC-jurisdictional, with different reporting, different manipulation standards and different enforcement history. Firms have been pursued by both for the same trade.

## Slide 4
03
Seven organised markets - and the third of the country that has none
There is no single US power market, and no single US power price
PJM
13 states · 67m people
Nodal · RPM capacity
Western Hub
MISO
15 states, N/C/S seams
Nodal · PRA
Indiana Hub
ERCOT
Texas, islanded
Nodal · energy-only
HB_NORTH
CAISO
California + EIM/EDAM
Nodal · bilateral RA
SP15 / NP15
SPP
Central plains, high wind
Nodal · no auction
North / South Hub
NYISO
New York, 15 zones
Nodal · ICAP
Zone J / Zone A
ISO-NE
Six states
Nodal · FCA
Mass Hub
ISO
Footprint
Design
Traded hub
No market at all
Most of the Southeast and much of the non-CAISO West remain vertically integrated. Utilities self-dispatch, trade bilaterally and are regulated on cost of service by state commissions. No LMP, no capacity auction, no public price curve.
And the map is moving
SPP's Markets+ and CAISO's EDAM are competing to organise the West. Whichever prevails redraws roughly a fifth of US load. Treat western market design as a live variable, not a constant.
Sources: ISO/RTO tariffs and public documentation; FERC Energy Primer. Accessed 30-Jul-2026.
Notes: The comparison a European reader will reach for is bidding zones, and it is the wrong one. A bidding zone has one price by construction. A nodal market has thousands of prices, of which a handful trade. The set of things called 'the PJM price' is large and its members are not interchangeable - slide 6 covers that specifically. The unorganised third of the country matters for a different reason: it is where a large share of new large-load siting is going, precisely because bilateral contracting with a vertically integrated utility can be faster than an interconnection queue.

## Slide 5
04
Locational marginal price, decomposed
LMP = energy + congestion + loss. The components are published, and the decomposition is what tab 4 of every market pack is built on
LMP = Energy + Marginal Cost of Congestion + Marginal Cost of Losses
The energy component is common to the whole market. Congestion and losses are what make one bus differ from another. Published LMP files give you congestion and losses directly, so energy is the residual.
Worked example - NYISO day-ahead, 29 July 2026, hour ending 17:00
Zone | LBMP $/MWh | Congestion | Losses | Energy (residual)
Zone J — N.Y.C. | 63.30 | 0.00 | 5.12 | 58.18
Zone A — WEST | 53.48 | 0.46 | −4.24 | 57.26
Zone G — HUD VL | 61.96 | 0.00 | 3.78 | 58.18
PJM proxy bus | 58.38 | 0.10 | 0.29 | 57.99
Zone J and Zone G show an identical energy component of 58.18. The whole $1.34 difference between them is losses. Zone A is nearly $10 cheaper than Zone J on the same energy price - that is what a nodal market prices and a bidding zone hides.
Why Europe has no equivalent
Under zonal design, congestion inside a zone is not priced. It is resolved after the market clears through redispatch, and the cost is socialised. Germany is the canonical case. In a nodal market that same congestion appears in the price, at every bus, every interval.
What this buys the risk manager
A hedge at a hub does not hedge a node. The residual - basis between your node and the hub you hedged at - is a real, sizeable, tradeable exposure. That is what congestion rights exist for, and it is the subject of the next slide.
Source: NYISO MIS public CSV, damlbmp/20260729damlbmp_zone.csv, retrieved live 30-Jul-2026. Energy component computed as LBMP less published congestion and loss components.
Notes: These are real numbers, pulled from the NYISO public feed during the build, not illustrative. That matters because it is also the first Gate 0 connection test in the programme - NYISO is keyless, so it proves outbound network access before any key-gated source is attempted. Note the sign convention on losses: Zone A shows negative marginal loss cost. Zone A is at Niagara, close to generation, so serving an extra MW there reduces system losses. Negative loss components are normal and are not an error.

## Slide 6
05
"The PJM price" is four different numbers
The most common and most expensive category error in North American power
Name | Type | What it is | Does it trade?
Western Hub | Hub | A defined basket of buses | YES - the traded index. Most bilateral and financial PJM volume settles here
PJM-RTO | RTO aggregate | Load-weighted average of the footprint | No. Quoted constantly, traded almost never
A zone (e.g. PSEG) | Zone | Load-serving aggregation | Retail and load settlement, not a generation hedge
A node (a specific bus) | Node | One physical bus | Where a generator actually settles. Basis to hub is the residual risk
The same trap, per market
ERCOT: HB_NORTH is a hub, LZ_NORTH is a load zone. Hubs settle generation and financials; load zones settle load. CAISO: SP15 trades, the system average does not. NYISO: Zone J is a zone that trades because the in-city constraint makes it one.
The control
The parameter workbook carries a PricingPoints registry - market, point, type, identifier, and whether it trades. Every price series in the programme must name its pricing point, and the verification harness refuses to aggregate across types.
A hedge executed at Western Hub against a generator sitting at a constrained node in western Pennsylvania is not a hedge. It is a hub position plus an unhedged basis position, and in a congested hour the basis is the entire P&L.
1 of 4
of the things called 'the PJM price' is actually tradeable
Sources: PJM, ERCOT, CAISO and NYISO tariff definitions and pricing-point registries. Accessed 30-Jul-2026.
Notes: This slide exists because the error is so easy to make from a data feed. EIA publishes a single hourly series per balancing authority. A newcomer pulls 'PJM' from EIA, computes a volatility, and has computed the volatility of a load-weighted average that nobody can trade - which is materially lower than the volatility of Western Hub, and much lower than the volatility of a constrained node. There is a second, related trap on the same feed: EIA balancing-authority footprints are not ISO market footprints. Use EIA for shape and cross-market comparability. Use ISO data for anything that settles.

## Slide 7
06
Congestion rights - the product class Europe does not have
FTR, CRR, TCC and ARR: different names, same idea, real market depth
An FTR pays the holder the difference in congestion component between two nodes, for a defined period and MW quantity. It is funded from the congestion revenue the ISO collects. It is a financial instrument settled against the market, not a physical right to move power.
PJM
FTR
+ ARR allocation to transmission customers
MISO
FTR
+ ARR
ERCOT
CRR
Point-to-point options and obligations
CAISO
CRR
Annual and monthly auctions
NYISO
TCC
Centralised auctions, up to several years
ISO-NE
FTR
Monthly and annual
SPP
TCR
Transmission congestion rights
Underfunding is the risk nobody expects
FTRs are paid from actual congestion revenue. If realised congestion is lower than the auction implied - because a line was rebuilt, or load moved - the ISO collects less than it owes and pays holders a pro-rata fraction. A fully-hedged position can still lose money.
Why it matters for the programme
This is genuinely new tab 4b, with no EU template to port. It is also the largest single gap between the two programmes, and the reason the Americas quant layer is not just the EU quant layer with different data.
Sources: PJM, MISO, ERCOT, CAISO, NYISO, ISO-NE and SPP market rules on financial transmission and congestion revenue rights. Accessed 30-Jul-2026.
Notes: European long-term transmission rights exist but are thin, mostly physical or physical-with-UIOSI, and allocated cross-border only. FTRs are a deep financial market with dedicated participants, secondary trading, and portfolio managers who do nothing else. Underfunding deserves emphasis because it breaks the mental model. A European reader thinks of a hedge as a claim on a counterparty. An FTR is a claim on a revenue pool. When the pool is short, everyone is paid a fraction. Historic funding ratios below 100% have occurred in several ISOs and are published - always check the funding ratio history before sizing a position.

## Slide 8
07
Two answers to the same question
How do you make sure the capacity is there in ten years - pay for it forward, or let scarcity prices do it?
Capacity markets — PJM, ISO-NE, NYISO, MISO
A forward auction procures MW of availability, separately from energy. Generators earn two revenue streams. The regulator sets a reliability requirement and the auction finds the price that meets it.
Energy-only — ERCOT, Alberta
No capacity payment at all. Investment is signalled entirely by expected energy and ancillary revenue, which means scarcity hours must be allowed to price very high.
PJM 2028/29 Base Residual Auction - the capacity model under stress
$325
per MW-day — cleared at the cap for the third consecutive auction
6,831 MW
short of the reliability requirement, despite clearing at the cap
$16.4bn
total cost of procured capacity
$554.72
where PJM estimates all zones would have cleared without the collar — nearly $30bn
The $325 cap was not a market outcome. It was imposed by agreement between FERC and the governors of all thirteen PJM states - a political intervention in a price-forming auction, in response to affordability pressure from load growth. For a risk manager that is the point: in a capacity market the administrative parameters are the dominant variable, and they can change between auctions.
Source: PJM Interconnection, 2028/2029 Base Residual Auction results; 138,318 MW UCAP procured. Accessed 30-Jul-2026.
Notes: Three consecutive auctions at the cap is the market telling you the reliability requirement cannot be met at any price the political system will tolerate. Clearing at the cap AND falling 6,831 MW short is a stronger statement still: even at the maximum permitted price, the MW did not show up. The European analogue is imperfect. Several EU member states run capacity remuneration mechanisms, but they are narrower, state-aid-constrained and generally not the primary investment signal. Here the capacity revenue can be a third or more of a peaker's income, so a change in auction parameters repricies the entire asset class overnight.

## Slide 9
08
How an energy-only market pays for capacity
ERCOT's Operating Reserve Demand Curve - scarcity priced, not procured
ORDC adds a price adder to energy as operating reserves tighten. The adder is derived from the probability of losing load at a given reserve level, multiplied by the value of lost load. As reserves fall the adder rises steeply, so the scarce hours carry the fixed-cost recovery that a capacity payment provides elsewhere.
High system-wide offer cap (HCAP)
$5,000/MWh
Lowered from $9,000 with effect from 1 January 2022
Low system-wide offer cap (LCAP)
greater of $2,000/MWh or 50 × the gas index
Set daily
Transition trigger
Peaker Net Margin threshold
Once PNM exceeds the threshold, HCAP holds for the balance of that day
Why the cap came down
Winter Storm Uri in February 2021 cleared at $9,000/MWh for days. The resulting settlement obligations bankrupted market participants and led directly to the cap reduction. The cap is not a technical parameter - it is the residue of a political event.
The design trade-off
Energy-only is cheaper in normal years and produces sharper investment signals. It also concentrates a generator's annual revenue into a handful of hours, which makes revenue extraordinarily weather-dependent and makes hedging both essential and difficult.
A generator with 7,000 Btu/kWh heat rate earns more in one $5,000/MWh hour than in three hundred ordinary hours. Every risk model for ERCOT is a model of the tail.
Sources: PUCT Substantive Rule 25.505; PUCT Project 52631, Review of the ERCOT Scarcity Pricing Mechanism. Verify current parameters at retrieval - they have moved twice since 2021 and are not to be carried from memory.
Notes: Note the instruction on the source line, which is a programme rule: price caps and scarcity parameters must be verified live and never carried from a previous build. The EU programme learned the equivalent lesson on UK Carbon Price Support, where a Batch 1 calculator would have been wrong from Cal-29 onward because the CPS abolition had not been picked up. The arithmetic in the closing line is worth doing on the board: at $5,000/MWh a 1 MW unit earns $5,000 in an hour. At a $40/MWh spark spread in ordinary conditions it earns $40. That is 125 ordinary hours, not 300, if you compare gross revenue - the 300 figure compares against a typical net margin. Either way the point stands and it is the reason ERCOT hedging is dominated by options rather than swaps.

## Slide 10
09
The load shock
After twenty years of flat demand, the fastest load growth since the 1970s - and it arrived faster than the queue can process it
Chart: 
| ERCOT large-load queue, Q1 2026 alone | ERCOT queue, end-2025 | PJM forecast new large load by 2030 | PJM forecast by 2037
GW | 198 | 233 | 55 | 100
2,600 GW
of generation and storage sitting in US interconnection queues in early 2026
>70%
of ERCOT's large-load queue is data centres
Why the queue is the binding constraint
Interconnection studies were designed for a world of a few large thermal plants a year. They now process thousands of applications with waits of five years and more. Generation cannot arrive on the timescale the load is arriving on, which is what turns a demand story into a price story.
What the ISOs are doing about it
Large-load interconnection processes, co-location rules for data centres sited at existing plants, and curtailable or flexible-load tariffs that let a data centre connect faster in exchange for being interruptible. All are live rulemakings - treat them as variables, not settled rules.
Europe has no equivalent. EU demand has been flat to declining, and its capacity debate is about replacing retiring thermal, not about serving new load. Every demand assumption ported from the EU programme is wrong here.
Sources: ERCOT large-load queue reporting via Latitude Media; PJM utility load forecasts; Ascend Analytics interconnection queue analysis. Accessed 30-Jul-2026. Queue volumes are applications, not commitments - attrition is historically high.
Notes: The caveat on the source line is important and should be said out loud: queue volumes are applications. Historic attrition in generation queues has run well above half, and large-load queues include speculative and duplicate applications where a developer applies at several sites for one project. The 198 GW figure is not 198 GW of load that will connect. But the direction is not in doubt, and the risk-relevant consequence is asymmetric: if even a fraction materialises on the current generation timeline, scarcity hours become more frequent in exactly the markets - ERCOT and PJM - where scarcity is either priced through ORDC or paid through a capacity auction already clearing at its cap.

## Slide 11
10
Four carbon regimes, one country
There is no federal carbon price. What exists instead is a patchwork, and it is repricing fast
RGGI
11 north-eastern states · power sector only
Auction 72 cleared $35.00 in June 2026
California – Québec (WCI)
Economy-wide cap-and-trade
2026 auction reserve price $27.94
Washington CCA
Economy-wide, linking
Linkage agreement signed 25 June 2026
Everywhere else
ERCOT, MISO, SPP, most of the Southeast
No carbon price at all
Chart: RGGI clearing price
| Auction 69 Sep 2025 | Auction 71 Mar 2026 | Auction 72 Jun 2026
$/short ton | 22.25 | 24.99 | 35
The CCR was exhausted
Auction 71 released the entire 2026 Cost Containment Reserve - 7.85 million allowances against an $18.22 trigger - and the market still cleared $35.00 three months later. A 57% rise in nine months.
UNIT TRAP: RGGI, WCI and WA CCA allowances are METRIC TONNES. EPA CAMPD reports emitted mass in SHORT TONS. Multiplying an unconverted CAMPD tonnage by an allowance price overstates carbon cost by 10.2%.
Sources: RGGI Inc. auction notices 69, 71 and 72; RGGI Third Program Review; CARB auction information; ICAP linkage announcement 25-Jun-2026. Accessed 30-Jul-2026.
Notes: Two forward-looking items. First, the RGGI Third Program Review tightens the regional cap from 2027 through 2037 and fixes the CCR at roughly 11.7 million allowances per tier - so the mechanism that failed to contain the 2026 price is being rebuilt, not abandoned. Second, the Washington-California-Quebec linkage signed on 25 June 2026 is expected to produce an operating linked market in 2027, which would create the second-largest compliance carbon market in the world. The unit trap is not hypothetical. It is a 10.2% error that produces a completely plausible-looking number, which is the most dangerous kind. The programme's parameter workbook enforces it: the CAMPD query converts to tonnes and outputs both columns, and the verification harness refuses a dollar-per-tonne multiplication until the mass basis is tagged.

## Slide 12
11
Tax credits as a negative carbon price
The largest single policy variable in the US build-out - and its central deadline passed three weeks ago
A production or investment tax credit lowers the effective cost of zero-carbon output. Economically it works like a negative carbon price - it changes the merit order by subsidising one side rather than taxing the other. Modelling US dispatch without it is modelling a different market.
On or before 4 Jul 2026
Wind and solar that began construction by this date keep the full credit on the original phase-out schedule
From 5 Jul 2026
Wind and solar beginning construction after this date must be placed in service by 31 Dec 2027 to claim anything
After 31 Dec 2027
45Y and 48E terminate for wind and solar placed in service beyond this date
2034 – 2036
Storage, fuel cells and other qualifying technologies phase down: 75% for construction starting 2034, 50% in 2035, nil from 2036
Foreign entity restrictions
From 2026, no specified foreign entity or foreign-influenced entity can claim 45Y, 48E or 45X. This is an ownership test, not a technology test, and it cuts across the supply chain.
Why it belongs in a risk deck
A credit cliff pulls construction starts forward and then stops them. Expect a build spike into the deadline, then an air pocket - visible in interconnection and equipment order data before it is visible in capacity.
Today is 30 July 2026. The begin-construction cliff is three weeks behind us, and its consequences are not yet in any published capacity series.
Sources: One Big Beautiful Bill Act; IRS Notice 2025-42 on beginning of construction; Treasury/IRS guidance on prohibited foreign entities. Accessed 30-Jul-2026. This is a summary for market context and is not tax advice.
Notes: The caveat on the source line is deliberate and should stay: this is a market-structure summary, not tax advice, and the begin-construction rules have detailed physical-work and five-percent safe harbours that decide individual projects. The risk-relevant shape is the air pocket. Deadline-driven credit regimes reliably produce a rush of qualifying starts followed by a gap. Because these projects take two to four years to reach commercial operation, the gap shows up in capacity additions in 2028-2030 - which is exactly the window in which PJM's capacity auction is already clearing at its cap and short of requirement.

## Slide 13
12
Heat rate, spark spread, and the 10% error waiting for you
The single most dangerous thing a European practitioner can carry into this market
EUROPE — LHV
Gas contracts settle in MWh. Turbine efficiency is quoted as a percentage on a lower-heating-value basis. A LHV/HHV correction of 0.9025 is applied where the two bases meet.
NORTH AMERICA — HHV
Gas is priced, sold and custody-metered in $/MMBtu on a higher-heating-value basis. Heat rate is quoted in Btu/kWh, also HHV. Both sides of the spread are already on the same basis.
Clean spark = Power ($/MWh) − HR (MMBtu/MWh) × Gas ($/MMBtu) − VOM − HR × 53.06/1000 × Allowance ($/tonne)
There is no 0.9025 term. Inserting one — the reflex of anyone who learned this in Europe — overstates the spread by about 10%.
The two programmes' CO2 factors are the same physics on different bases
Step | Value
EU programme factor, LHV thermal | 0.20196 tCO2/MWh
÷ 3.412142 MMBtu/MWh | 0.059188 t/MMBtu LHV
× 0.9025 (LHV → HHV) | 53.42 kg/MMBtu HHV
EPA published factor, HHV | 53.06 kg/MMBtu
Agreement | 0.67%
How the programme enforces it
GetConvention() refuses to return any unit basis whose Locked flag is not set. The workbook carries this bridge as live formulas, and the verification harness fails the build if the agreement exceeds 1%. Tested by deliberate sabotage: pasting the LHV number over the EPA factor produces a 9.75% disagreement and a hard fail.
Sources: EPA GHG Emission Factors Hub; EU Energy Programme locked conventions. 1 MWh = 3.412141633 MMBtu, exact by definition of the Btu(IT).
Notes: This slide is the reason the two programmes can safely sit side by side. The failure mode is not that someone does the arithmetic wrong - it is that they do the arithmetic right, using a convention from the other continent, and get a number that looks entirely reasonable. The 0.67% residual between 53.42 and 53.06 is not error to be reconciled away. The EU figure is a programme convention derived from IPCC 2006 defaults; EPA's is a US-specific factor reflecting the composition of pipeline-quality US gas. They should be close but not identical, and the fact that they agree to under 1% is the check that both are being applied on the basis they were meant for.

## Slide 14
13
Where the data comes from, and what is honestly not verified
Verification status is stated per source. Where a call could not be made, it says so
Source | What it gives | Auth | Status 30-Jul-2026
NYISO MIS | Day-ahead and real-time LBMP with components | None | VERIFIED LIVE — full 29-Jul file returned
ERCOT Public API | Settlement point prices, 35 portal reports | OAuth + key | CONFIRMED — registration required
EPA CAMPD | Unit-level hourly heat input, CO2, gross load | Free key | Not verified — no key held
EIA Open Data v2 | Capacity, generation, demand, gas | Free key | Not verified — no key held
PJM Data Miner 2 | LMP with components, auction results | Free key | Not verified
CAISO OASIS | LMP | None | ZIP wrapper — download step required
MISO | Real-time and market data | None | FAILED — legacy route returned no data
Regional gas indices | Waha, AECO, Algonquin, SoCal | Licensed | NOT SOURCED — same rule as EU curves
The highest-value source
EPA CAMPD has no European equivalent. Unit-level hourly heat input and CO2 lets the implied heat rate of the marginal unit be measured from data rather than assumed. It should anchor the quant layer.
The blocker
MISO's legacy data route returned no data on 30 July 2026 — it has moved. MISO is in Batch 1, so this must be resolved before Batch 1 starts. It is recorded as BLOCKED in the market registry rather than quietly worked around.
V-codes, carried unchanged from the EU programme: LIVE (retrieved, dated) · SRC (published, cited) · CONF (primary text) · CALC (in-workbook formula) · GAP (known missing, never estimated into).
42 / 42
verification checks passing on the Batch 0 workbooks
4 / 4
deliberate sabotage attempts caught by the harness
Source: Americas Energy Programme source registry and verify_us.py output, 30-Jul-2026.
Notes: The sabotage testing is the part worth explaining. The EU programme's most important defect was a verification harness that passed vacuously - LibreOffice was writing its output over its own input, so 'zero errors' was measured on a workbook that had never been evaluated. A guard you have never seen fail is a guard you cannot trust. So the Americas harness ships with a negative test that deliberately breaks the workbook four ways - pasting the LHV factor over the EPA one, inserting the European correction into a US spark spread, renaming a registry column, and clearing a locked convention - and asserts each is caught. All four are, against a clean baseline.

## Slide 15
14
What your European experience buys you, and what it costs you
The honest delta - read this before opening the first market pack
Dimension | Europe | North America | Verdict
Price formation | Zonal, one price per bidding zone | Nodal LMP, thousands of buses, a handful trade | REBUILD
Congestion | Socialised, resolved by redispatch after clearing | Priced in every LMP; hedged with FTR/CRR/TCC | NEW — no template
Resource adequacy | Patchwork of national CRMs | Forward auctions in four ISOs, energy-only in two | REBUILD
Gas calorific basis | LHV | HHV | INVERT — 10% if carried
Mass | Metric tonnes | Short tons at EPA, tonnes for allowances | CONVERT — 10.2%
Carbon | One instrument (EU ETS), plus CBAM and ETS2 | Four regimes and a large no-price zone | REBUILD
Regulator | ACER + NRAs; REMIT / EMIR / MiFID II | FERC + NERC + state PUCs; CFTC for derivatives | REBUILD
Demand | Flat to declining | Fastest growth since the 1970s | INVERT
Hydro-led market | Nordics reservoir and EPAD | Brazil PLD by submarket, cost-based dispatch | TRANSFERS
Split organising logic | Nordics: structure country-first, price zone-first | MISO North/Central/South; Brazil submarkets | TRANSFERS
Dated policy switch | UK CPS abolition, April 2028 | 45Y/48E cliff; RGGI review; WCI linkage | TRANSFERS
Net-producer formulas | Suppressed for Norway and Denmark | Suppressed programme-wide — US and Canada both net | TRANSFERS
Four things transfer cleanly. Eight need rebuilding, and two of those are silent 10% errors that produce entirely plausible numbers. That asymmetry is why this programme has its own parameter structure rather than reusing Europe's.
Source: Americas Energy Programme plan §2, structural deltas. 30-Jul-2026.
Notes: End on the asymmetry. The things that transfer are the analytical habits - reconciling components to totals, refusing to estimate into a gap, treating dated policy switches as first-class objects, suppressing a formula where the sign convention breaks. The things that do not transfer are the numbers and the market design. That is the right way round. It means the EU programme's value here is methodological rather than factual, and it is why the verification standard was ported first, before any content.